| Starting reinforcing-sewing No.54 No.55 | Forward sewing and reverse stitching joint |  | Reverse stitch number Become less and shorter，To adjust the parameters to a higher value.No.54 |  | Forward sewing number Become less and shorter，Adjust the parameters to lower values No.54 |
| --- | --- | --- | --- | --- | --- |
|  | Reverse sewing and forward stitching joint |  | Forward sewing number Become less and shorter，To adjust the parameters to a higher value No.55 |  | Reverse stitch number Become less and shorter，Adjust the parameters to lower value No.55 |
| ending reinforcing-sewing No.57 No.58 | Forward sewing and reverse stitching joint |  | Reverse stitch number Become less and shorter，To adjust the parameters to a higher valueNo.57 |  | Forward sewing number Become less and shorter，Adjust the parameters to lower valuesNo.57 |
|  | Reverse sewing and forward stitching joint |  | Forward sewing number Become less and shorter，To adjust the parameters to a higher value No.58 |  | Reverse stitch number Become less and shorter，Adjust the parameters to lower value No.58 |
| continuous reinforcing-sewing No.60 No.61 | Forward sewing and reverse stitching joint |  | Reverse stitch number Become less and shorter，To adjust the parameters to a higher value No.60 |  | Forward sewing number Become less and shorter，Adjust the parameters to lower valuesNo.60 |
|  | Reverse sewing and forward stitching joint |  | Forward sewing number Become less and shorter，To adjust the parameters to a higher value No.61 |  | Reverse stitch number Become less and shorter，Adjust the parameters to lower value No.61 |
| Function | Button | Described |  |
| Starting reinforcing-sewing |  | Execute starting reinforcing-sewing 2 times, to and fro. |  |
| ending reinforcing-sewing |  | Execute ending reinforcing-sewing 2 times, to and fro. |  |
| continuous reinforcing-sewing |  | 1、Press treadle ahead for automatic sewing, to and fro, which is set at D and can reach 15times.(F) 2、Continuous reinforcing-sewing is in trigger mode by default, treadle doesn’t need to be kept being pressed, and corresponding trigger light of preset sewing is solid lit. 3、Previous ending reinforcing-sewing setting is invalid if this function is valid. |  |
| parameter setting |  | 1.For preset sewing. Trigger treadle and the system will automatically conduct sewing at E, F, G, H sections; the treadle doesn’t need to be kept being pressed.2.Solid light for continuous reinforcing-sewing mode means that it is trigger mode by default. |  |
| thread- cutting |  | Set or cancel thread-cutting function. |  |
| Needle position |  | Set the needle position shortcut keys，Key is effective for needle，The cancel key function is set to stop pin。. |  |
| The middle presser foot |  | Presser foot to set shortcut keys: set or cancel the presser foot function. |  |
| Shear line pressure foot |  | The shear line and presser foot set shortcut keys: set or cancel trimmer and presser foot function. |
| Soft start |  | Soft start to set shortcut keys: set or cancel the pedal soft start function. |
| Pinnumberset/check choice |  | Implementation of this key, circulating switch display 3 pin number to set the display value upper end:A、B、C、DPeriod of pin number,Light corresponding level; Middleend:E、FPeriod of pin number,Light corresponding level; lower extreme:G、HPeriod of pin number,Light corresponding level; Corresponding to A D period of pin number, can set range 0 ~ 15 needle, B paragraph C pin number, can set range 1 ~ 15 needle, among them, the liquid crystal display A B C D E F on each for 10 11 12 13 14 15 stitches. |
| parameter setting |  | 1.Entering different parameter level On the sewing setting interface, the user can press the button P to enter the Parameter Interface, then the Level I parameters in the parameter list will display. On the sewing setting interface, the user can keep pressing the button for a few seconds to enter the Password Entering Interface. After entering the right maintenance password, then the user can press the button P to enter the Parameter Interface, now the Level I and Level II parameters in the parameter list will display. Password setting On the sewing setting interface, the user can keep pressing the button P for a few seconds to enter the Password Entering Interface, and press the button combination of “burst button + soft start button” to enter the Password Resetting Interface. The three indicators (respectively are Indicator S1, S2 and S3 from left to right/before three lamp, among which one is on) corresponding to the button S indicates the current status. S1 lights up, old password input, ending the key combination trigger key + tangent key, if the correct password into the password reset interface (mistakes have stayed the S1 state), and at the same time S2 light, prompting the input new password and click confirm S3 S key input again when the light is the new password, according to S key after two input if consistent, then set success, return to parameter interfaceIf the new passwords entered are not the same, the Indicator S1 will be on and the LC screen will be reset, and the user shall enter the old password again. If the user presses the button P, the user will be brought back to the interface parameters and no modification will be saved. You can choose from the numbers of 0 to 9 or the letters of A to F for every single character of the password. Please do keep the new password in mind. |
| Teaching function |  | Set or cancel the teaching function. |
| Sewing set program |  | The number of needles sewing set，Set up a total of 15 segment needle number P1~PF. |
| speed key |  | Speed down. Keeping pressing to lower speed, the display will automatically switch to speed set. Simple seam, free seam effective. |
|  |  | Speed up. Keeping pressing to increase speed, the display will automatically switch to speed set.Simple seam, free seam effective. |

# Text boxes

Teaching function：

In the long slot (a, four, program seam) mode, long press "T" one second, you can enter the teaching interface, this interface has buttons: T key, two groups of add-substract key, fill needle key. Role is as follows:

Add-substract key 12: change teaching segments, segment numerical only to accumulate (into the next section teaching automatically save the last needle numerical reduction), '-' key is invalid. Note: when the pedal operation, the key is invalid;

Add-substract key 34: modify teaching pin number, to stop running when the adjust pin number. Fill needle keys: press can manually fill needle, needle change.

T: exit show interface, complete the current segment number teaching (section numerical covering the original mode).

After the pedal shear line, will directly from the show and save the needle numerical, before returning to the fixed length of stitch pattern.

4.Operation box use

# 1. Safety instruction

## Please read the operation manual and related sewing machinery datasheet carefully before correct use.

## 1.1 (1) Power voltage and frequence: please refer to motor and control box nameplate.

## (2) Interference  from electromagnetic wave:please keep far away strong magnetic or high radiation environment in order to avoid obstructions and make to misoperation.

## (3) Grounding: to avoid the noise obstructions or leakage of electricity accident(inculding sewing machine,motor,control box and positioner.

## 1.2 Please make sure power off at least 1min and then can open control box cover, because there are dangerous high voltage.

## 1.3 Please turn off the power while repairing or wearing needle in order to protect operater’s safty,

1.4   Used where potential dangers exist.

Used where high voltage and electric danger exist.

1.5 Product warranty period of one year on condition that this machine is operated correctly and no man-made damage.

-2-

3．System Info

Operation panel default mode, press the button at the same time in P made sewing needle trigger select key, enter the system monitoring state through the +-key choose need to look at the project, according to the S button to enter/exit the selected projects such as the need to exit monitoring interface, according to P keys can be.

| show frame numbers | Item Name | unit |  | show frame numbers | Item Name | unit |
| --- | --- | --- | --- | --- | --- | --- |
| JJ | Plan number | piece |  | U6 | Motor initial Angle | limit |
| U1 | speed of motor control | rpm |  | U7 | Master control program version/ Head type | / |
| U2 | Motor Current | 0.01A |  | U8 | Head type/ Master control program version | / |
| U3 | Motor Voltage | V |  | U9 | Dsp no | / |
| U4 | Pedal voltage | 0.01V |  | vEr | Operation box version of the program | / |
| U5 | Mechanical Angle with | limit |  | TYPE | Software no | / |

| No | Project | Content | Setting range | default value | Level |
| --- | --- | --- | --- | --- | --- |
| 1 | Sewing speed | Set sewing speed | 200～3000rpm | 2000 | I |
| 2 | Soft-start function | 0：No soft-start function 1~99：Soft start stitches | 0~99 | 3 | I |
| 3 | Ornamental bartacks | 0： Invalid 1： Effective | 0/1 | 1 | I |
| 4 | Fixed-length seam sewing speed | Set fixed-length seam sewing speed | 200～3500rpm | 2000 | I |
| 5 | Sewing mode | 0： Free sewing 1： Simple Sewing | 0/1 | 0 | I |
| 9 | Reverse limitted feed speed | Reverse limitted feed speed,when the manual switch closed | 500～1500rpm | 700 | I |
| 19 | Function of stop after bartack at the start of sewing | Function of stop after bartack at the start of sewing 0： Invalid 1： Effective | 0/1 | 0 | I |
| 20 | The manual switch function of the reverse feed stitching of sewing | 0：Only reverse feed stitching 1：And needle compensation 2：Only reverse feed stitching , standby does not work | 0/1/2 | 0 | I |
| 21 | Soft-start speed 1 | The first stitch speed | 100～3000rpm | 400 | I |
| 22 | Soft-start speed 2 | The second stitch speed | 100～3000rpm | 600 | I |
| 23 | Soft-start speed 3 | The third stitch speed | 100～3000rpm | 600 | I |
| 24 | Function of soft-down of presser foot | 0: Invalid 1: Valid | 0/1 | 0 | I |
| 25 | Enable presser foot lift | 0: Disable 1: Enable | 0/1 | 1 | I |
| 27 | Up –position function | 0: Invalid 1: Valid | 0/1 | 0 | I |
| 28 | Safety switch signal mode | 0: Normally open 1: Normally closed 2: No protection | 0/1/2 | 0 | I |
| 29 | The time of soft-down of pressure foot | The time of soft-down of pressure foot(time longer,down more slower) | 50～500ms | 300 | II |
| 30 | The bottom line magnification setting | 0：Invalid 5/10/15/20：Bottom line rate | 0/5/10/15/20 | 0 | I |
| 31 | Initial baseline setting | Initial baseline setting | 200～4000 | 1600 | I |
| 32 | Ornamental bartacks pause time | Ornamental bartacks pause time | 5～500ms | 50 | I |
| 34 | Standard bartacks,pedal speed source choice | 0: automatic standard bartacks speed 1: pedal analog speed | 0/1 | 0 | II |
| 35 | Piece-rate setting | 0:No piece-function 1～50:(Piece multiples)+1 | 0～20 | 0 | I |
| 36 | Initial set piece count | Initial set piece count | 0～1000 | 100 | I |
| 41 | Slow speed | The lowest pedal speed | 100～400rpm | 200 | I |
| 42 | Pedal curve selection | 0： Normal 1： Slow acc. 2： Fast acc | 0/1/2 | 0 | I |
| 44 | Cutting speed | Cutting speed | 100～400rpm | 200 | I |
| 45 | Reverse limitted feed speed enable | 0： Disable 1： Enable | 0/1 | 0 | I |
| 46 | Delay Sewing time,when presser foot down | Delay Sewing time,when presser foot down | 0～800ms | 50 | II |
| 47 | Time of presser foot magnet full voltage output | Time of presser full voltage output | 0～800ms | 150 | II |
| 48 | Presser foot magnet voltage output duty cycle | Presser foot voltage output duty cycle | 0～100 | 40 | II |
| 49 | Presser foot magnet lift holding time | Presser foot magnet lift holding time | 1～60(s) | 12 | II |
| 50 | Time of reverse feed stitching magnet full voltage output | Time of reverse feed stitching full voltage output | 0～800ms | 150 | II |
| 51 | Reverse feed stitching magnet duty cycle | Reverse feed stitching magnet duty cycle | 0～100 | 45 | II |
| 52 | Reverse feed stitching magnet holding time | Reverse feed stitching magnet holding time | 1～60(s) | 12 | II |
| 53 | Speed of bartack at the start of sewing | Speed of bartack at the start of sewing | 100～3000rpm | 700 | I |
| 54 | Bartack at the start of sewing compensation 1 | Bartack at the start of sewing compensation 1 | 0～100 | 20 | I |
| 55 | Bartack at the start of sewing compensation2 | Bartack at the start of sewing compensation 2 | 0～100 | 12 | I |
| 56 | Speed of bartack at the end of sewing | Speed of bartack at the end of sewing | 100～3000rpm | 700 | I |
| 57 | Bartack at the end of sewing compensation 1 | Bartack at the end of sewing compensation 1 | 0～100 | 20 | I |
| 58 | Bartack at the end of sewing compensation 2 | Bartack at the end of sewing compensation 2 | 0～100 | 12 | I |
| 59 | Overlapped sewing speed | Overlapped sewing speed | 100～3000rpm | 700 | I |
| 60 | Overlapped sewing speed compensation 1 | Overlapped sewing speed compensation 1 | 0～100 | 20 | I |
| 61 | Overlapped sewing speed compensation 1 | Overlapped sewing speed compensation 2 | 0～100 | 12 | I |
| 62 | Pedal travel upon start | Pedal position upon start Travel relative to medium pedal | 10～50 | 25 | II |
| 63 | Pedal travel upon acceleration | Pedal position upon start acceleration Travel relative to medium pedal | 10～100 | 50 | II |
| 64 | Pedal travel at highest rotation speed | Pedal position at highest rotating speed Travel relative to medium pedal | 10～150 | 110 | II |
| 65 | Pedal travel upon presser foot lift | Pedal position upon pedal lift Travel relative to medium pedal | -100～-10 | -30 | II |
| 66 | Pedal travel upon presser foot lowering | Pedal travel from presser foot lowering position to neutral position Travel relative to medium pedal | 5～50 | 10 | II |
| 67 | Pedal travel 1 upon thread trimming | Pedal position upon start trimming without presser foot function Travel relative to medium pedal | -100～-10 | -30 | II |
| 68 | Pedal travel 2 upon tread trimming | Pedal position upon start thread trimming with presser foot function Travel relative to medium pedal | -100～-10 | -60 | II |
| 69 | Down needle positioning position | To adjust down needle position | 0～240 | 60 | I |
| 70 | Reverse needle lift function | 0： Disable 1： Enable | 0/1 | 0 | I |
| 71 | Reversal of needle lift angle | Reversal of needle lift angle | 0～90° | 45 | I |
| 75 | Needle position adjustment | Needle position adjustment | 0～240° | 214 | I |
| 76 | Stop needle position minor adjustment | Stop needle position minor adjustment | 90～110 | 100 | I |
| 77 | Needle bar maximum angle | Needle bar maximum angle | 270～360 | 290 | I |
| 78 | Key switch function selection | 0：Fixed sewing reverse 1：Supplementary needle | 0/1 | 0 | I |
| 79 | return to factory-set parameter | 5: restore the current level factory parameters 8: restore the current level and sewing factory parameter set According to S button, select yes, then press the S key execution | 0～15 | 0 | I |
| 80 | highest speed of sewing | highest speed of sewing | 200～3500spm | 2500 | II |
| 82 | Set period of use | 0：Disable； 1～1000(Take hours as a unit) | 0～1000 | 0 | II |
| 83 | Aggravating function/ Machine needle emphasis function | Needle wear through cloth when used 0: invalid; 1 ~ 15 strength regulation | 0～15 | 0 | II |
| 84 | Reduce noise | 0～15 Reduce noise | 0～15 | 0 | II |
| 85 | Cutting magnet pull angle | Cutting magnet pull angle | 150～200 | 60 | II |
| 86 | Power angle of shear line | To set power angle of shear line | 200～300 | 260 | II |
| 87 | Cutting magnet release angle | Cutting magnet release angle | 300～360 | 340 | II |
| 88 | Loose magnet pull angle | Loose magnet pull angle | 150～250 | 300 | II |
| 89 | Up dead position angle | Up dead position angle | 270～360 | 320 | II |
| 90 | Line slack holding time | Line slack holding time | 1～60 | 1 | II |
| 92 | Pedal presser foot lift confirm time | Pedal presser foot lift confirm time | 10～300ms | 80 | II |
| 93 | dial line / clip line Type selection | Type selection；0：dial line 1：clip line | -15～15(0.1) | 0 | II |

2.System parameter table

5.Standard needle stitch compensation adjustment

5. Error codes

| Error Code | Contents | Possible reasons | Checking and treatment |
| --- | --- | --- | --- |
| E011 E012 E013 E014 | Motor signal error | Motor position sensor signal failure | If electric engine plug is well contacted; if electric engine signal detecting device has been broken; if sewing machine handwheel correctly installed. |
| E015 | Model type error | Unable identify operating box model type | Check operating box |
| E021 E022 E023 | Motor overload | motor stall motor overload | If electric engine plug is well contacted; if machine head or thread-cutting mechanism has been blocked completely;f materials are too thick; Electrical signal detection signal whether the normal. |
| E101 | Hardware drivers fault | Current detection abnormal Driving hardware error | Current detection loop system is working properly;Whether the damage to the device driver. |
| E111 E112 | Voltage too high | High input voltage Brake circuit fault Voltage detection error | System into line voltage is too high; Braking resistance are working properly; System voltage detection circuit are working properly. |
| E121 E122 | Voltage too low | Actual low voltage Voltage detection is wrong | If the voltage on the inlet wire is too low Whether the system voltage detection circuit the normal work. |
| E131 | Current circuit fault | Current detection abnormal | Current detection loop system is working properly. |
| E133 | Oz circuit fault | Oz circuit fault | Oz circuit system is working properly. |
| E151 | Magnet circuit error | Over current magnet circuit | If machine head magnet suffers short circuit Electromagnet circuit is working properly. |
| E201 | over current | Current detection error | Current detection loop system is working properly Electrical signal is normal. |
| E211 E212 | Abnormal motor operation | Current or voltage detection error | If electric engine plug is well contacted; If electric engine signal is matched. |
| E301 | Communication error | Sci circuit error | if operation box plug is well contacted; if operation box components are damaged. |
| E302 | Operation inner failure | Sci circuit error | To check whether the operating box is damaged.. |
| E402 | Pedal ID fault | Pedal verification fault | Pedal connection is loosen. |
| E403 | Pedal zero position fault | The pedal zero position over range | The pedal is damaged or it is not under stop state when correction. |
| E501 | Safety switch fault | Safety switch effective | Put down the head or check turned up switch. |
| P.oFF | Power off Display | Power off | Wait for power supply to resume. |

Note: 1. Sewing abnormal action (speed electromagnet work abnormal) : in the control interface view model is correct;

2. Turn up E501 fault when: sure it is normal to switch detection, temporary use can change the P-28 parameters;

3. If the above according to check the project cannot rule out fault, please seek technical support.

WR58L High series manual V1.2

V1.2

-1-