安全指示

- 在安装或使用本产品前，使用者必须详细阅读本操作手册。

- 本产品须由受过正确训练的人员来安装或操作。安装作业时必须关闭所有电源，切记不可带电操作。

3） 所有标有符号的指示，必须特别注意并按照说明书上的执行，以免造成不必要的损害。

4） 为安全起见，禁止以延长线作电源座供应二项以上的电器产品使用。

5） 在连接电源线时，必须确定工作电压低于AC 250V，且符合本产品标识中规定的额定电压值。

※注意  ：电控箱电源规格如为AC220V时，请勿插接至AC380V的电源插座上，否则将出现异常且电机无法动作。此时请立即关闭电源开关，重新检查电源。持续供应380V超过五分钟以上，将可能烧损电控箱内器件，而危及人身安全。

6） 请不要在日光直接照射的场所、室外及室温45℃以上或0℃以下的场所操作。

7） 请不要在暖气（电热器）旁、有露水的场所及在相对湿度10%以下或90%以上的场所操作。

8） 请不要在灰尘多的场所、具有腐蚀性物质的场所及有挥发性气体的场所操作。

9） 请注意所有电源线、信号线、接地线等接线时不要受压或过度扭曲，以确保使用安全。

10）电源线的接地端须以适当大小的导线和接头连接到生产工厂的系统地线，此连接必须被永久固定。

11）所有可转动的部分，必须以所提供的零件加以防范露出。

12）在安装完成第一次开电后，先关闭切线功能以低速操作缝纫机并检查转动方向是否正确、运转是否稳定。

13）在进行以下操作前，请先关闭所有电源：

1.在控制箱与马达上插拔任何连接插头时。

2.穿针线时。

3.翻抬缝纫机机头时。

4.修理或做任何机械上的调整时。

5.机器闲置不用时。

14）修理或高层次的保养工作，仅能由受过训练的机电技师来执行。

所有维修用的零件，须由本公司提供认可，方可使用。

15）使用本产品请远离高频电磁波和电波发射器等，以免所产生的电磁波干扰伺服驱动装置而发生误动作。

16）请不要以不适当物体来敲击或撞击本产品及各装置。

保修期限

本产品保修期限为购买日期起一年内或出厂月份起两年内。

保修内容

本产品在正常情况使用且无人为操作失误的前提下，于保修期间无偿为客户维修使能正常操作。

但以下情况于保修期间将收取维修费用：

1.不当使用包括误接高压电源、将产品移做其它用途、自行拆卸、维修、更改、或不依规格范围使用、进水进油及插入异物于本产品。

2.火灾、地震、闪电、风灾、水灾、盐蚀、潮湿、异常电压及其它天灾或不当场所造成的损害。

3.客户购买后摔落本产品，或客户自行运输（或托付运输公司）造成的损害。

* 本产品在生产及测试上皆尽最大努力和严格控制使其达到高品质及高稳定的标准，但外部的电磁或静电干扰或不稳定的供应电源，仍可能对本产品造成影响或损害，因此操作场所的接地系统一定要确实做好，并建议用户安装故障安全防护装置（如漏电保护器）

1．按键显示及操作说明

1.1按键说明

| 名称 | 按键 | 注明 |
| --- | --- | --- |
| 进入参数区功能键 |  | 一般模式下按【P】键进入用户参数模式 |
| 进入和确定存储保存键 |  | 进入参数项及其内容值如经调整变更后，需按下【S】键予以保存确认。 |
| 设置数值递增/参数递增键 |  | 1.A、B、C、D、E、F、G、H的设定针数增加。 2.参数选择区内当参数递增键。 3.参数内容区内当设定数值递增键。 4.主界面下点击可增大缝纫速度。 |
| 设置数值递减/参数递减键 |  | 1.A、B、C、D、E、F、G、H的设定针数减少。 2.参数选择区内当参数递减键。 3.参数内容区内当设定数值递减键。 4.主界面下点击可减小缝纫速度。 |
| 起始 / 终止回快捷缝键 |  | 若点击，切换执行起始回缝B段、执行起始回缝（A、B段）1次或执行起始回缝（A、B段）2次； 若长按，增加屏幕背光亮度； |
|  |  | 若点击，切换执行终止回缝C段、执行终止回缝（C、D段）1次、执行终止回缝（C、D段）2次； 若长按，降低屏幕背光亮度； |
| 自由缝快捷键 |  | 一旦踏板往前踏下就正常车缝，当踏板回到中立时，立即停止车缝。当踏板往后踏时，就自动完成切线 / 扫线等动作。 |
| 一段定针缝快捷键 |  | 执行E段定针缝功能，当显示屏显示图标时，激活E段定针缝功能。 |
| 连续回缝快捷键 |  | 1.一旦踏板往前踏下，就自动执行来回的连续回缝动作，来回次数由E段设定。∴前踏之后即自动执行此功能到完成切线为止，中途不会停止车缝，除非将踏板往后踏可解除动作。 |
| 多段定针缝快捷键 |  | 多段定针缝功能，当显示屏显示图标时，激活多段定针缝功能。 |
| 触发自动键 |  | 1.在自由缝的式样中：按下此键无功能。 2.在定针缝的式样中按下此键：当踏板一经往前踏下触发，则自动执行E，F段或G，H段中所设定的针数，直到段内针数完成后自动停止。再逐一触发踏板，则自动执行下一段所设定的针数直到自动完成切线、扫线等动作为止。相应图标不亮时，表示关闭相应功能。 3. 若长按，可恢复出厂设置； |
| 抬压脚快捷键 |  | 1、图标亮时，切完线后压脚自动抬起。 2、图标亮时，车缝中马达停止时压脚自动抬起。 3、2个图标都亮时，切完线后和车缝中马达停止时压脚都自动抬起。 4、当2图标都不亮时，无自动抬压脚功能。 |
| 夹线功能/抬压脚时松线功能快捷键 |  | 1、相应图标亮时，夹线功能打开。 2、相应的图标不亮时，无夹线功能。 |
| 切线功能快捷键 |  | 1.设定使用或取消切线功能。 2.相应图标不亮时，表示关闭相应功能。 |
| 慢速起缝快捷键 |  | 1、相应图标亮时，慢速起缝打开。 2、相应的图标不亮时，无慢速起缝功能。 |
| 停针位切换键 |  | 1：图标亮了表示停车时在上停针位 2：图标亮表示停车时在下停针位 |
| 补针键 |  | 若点击，可进行补针 |

2.参数表

| 参数项 | 中文说明 | 范围 | 初始值 | 内容值名称说明与备注 |
| --- | --- | --- | --- | --- |
| P01 | 最高转速（rpm） | 100-3700 | 3700 | 车缝时的最高转速设定 |
| P02 | 加速曲线调整（%） | 10-100 | 80 | 控速器爬升斜率设定 斜率值愈大，速度愈陡；斜率值愈小，速度愈慢 |
| P03 | 针停定位选择 | UP/DN | DN | UP：上停针；DN：下停针 |
| P04 | 起始回缝速度（rpm ） | 200-3200 | 1800 | 前段回缝（起始回缝）时的速度设定 |
| P05 | 终止回缝速度（rpm ） | 200-3200 | 1800 | 后段回缝（终止回缝）时的速度设定 |
| P06 | 连续回缝速度（rpm） | 200-3200 | 1800 | 连续回缝时的速度设定 |
| P07 | 慢速起缝速度（rpm） | 200-1500 | 400 | 慢速起缝时的速度设定 |
| P08 | 慢速起缝针数 | 0-99 | 2 | 慢速起缝时的针数设定 |
| P09 | 自动定针缝速度（rpm） | 200-4000 | 3700 | 定针缝【P34.】设定在A状态的速度设定（或选针盒AUTO键有按下时的速度设定） |
| P10 | 定针缝后自动执行终止回缝功能（不补针功能设定） | ON/OFF | ON | ON：在执行完最后一段定针缝后，将自动执行终止回缝动作。 注：即在任何缝制模式下，终止回缝前不能作补针功能。 OFF：在执行完最后一段定针缝后，将无法自动执行终止回缝功能，必须重新再作前或全后踏动作时才可执行终止回缝或进行补针功能。 |
| P11 | 手按回缝时功能模式选择 | J/B | J | J：JUKI方式（在车缝中和中途停止时均执行倒缝） B：BROTHER方式（即在车缝中执行倒缝动作，在停止时执行补针动作） |
| P12 | 起始回缝运动模式选择 | 0-1 | 1 | 起始回缝段，倒退电磁线圈动作时机： 0：受踏板控制，可任意停止与启动； 1：轻触踏板，自动执行回缝动作 ； |
| P13 | 起始回缝结束点操作模式选择 | CON/STP | CON | CON：起始回缝段完成后，自动连续下一段功能 STP：起始回缝段针数完成后自动停止 |
| P14 | 慢速启动 | ON/OFF | ON | ON：慢速启动功能开启 OFF：慢速启动功能关闭 |
| P15 | 补针方式 | 0-4 | 2 | 0：半针；1：一针；2：连续补半针；3：连续补一针；4: 连续补针, 快速停车 |
| P16 | 手动倒缝时最高转速 （rpm） | 200-3200 | 2000 | 手动倒缝时的最高速度设定 |
| P18 | 起始回缝补偿1 | 0-200 | 131 | 起始回缝A段针迹补偿，0～200动作逐步滞后；数值越大，A短最后一针越长，B段第一针越短 |
| P19 | 起始回缝补偿2 | 0-200 | 165 | 起始回缝B段针迹补偿，0～200动作逐步滞后；数值越大，B段最后一针越长 |
| P20 | 终止回缝运动模式选择 | 0-2 | 1 | 起始回缝段，倒退电磁线圈动作时机： 0：受踏板控制，可任意停止与启动； 1：轻触踏板，自动执行回缝动作 ； 2：停顿模式 |
| P21 | 脚踏板前踏点电压 | 30-1000 | 520 |  |
| P22 | 脚踏板中踏点电压 | 30-1000 | 480 |  |
| P23 | 脚踏板半反踏点电压 | 30-1000 | 240 |  |
| P24 | 脚踏板反踏点电压 | 30-500 | 110 |  |
| P25 | 终止回缝补偿3 | 0-200 | 131 | 终止回缝C段针迹补偿，0～200动作逐步滞后；数值越大，C段第一针越短 |
| P26 | 终止回缝补偿4 | 0-200 | 165 | 终止回缝D段针迹补偿，0～200动作逐步滞后；数值越大，C段最后一针越长，D段第一针越短 |
| P27 | 辅助功能设置 | N10 背光亮度设置 | 3 |  |
|  |  | N11 背光熄灭时间设置（s） | 30 |  |
| P28 | 连续回缝运动模式选择 | 0-2 | 1 | 连续回缝段，倒退电磁线圈动作时机： 0：受踏板控制，可任意停止与启动； 1：轻触踏板，自动执行回缝动作 ； 2：停顿模式 |
| P29 | 切线后刹车力度 | 1-45 | 20 |  |
| P30 | 厚料加力力度 | 0-100 | 0 | 数值越大力度越大，调整过大可能会引起电机异常。 |
| P31 | 剪线加力力度 | 0-100 | 30 | 数值越大力度越大，调整过大可能会引起电机异常。 |
| P32 | 连续回缝补偿5 | 0-200 | 121 | 起始回缝A（C）段针迹补偿，0～200动作逐步滞后；数值越大，A（C）段最后一针越长；B（D）段第一针越短 |
| P33 | 连续回缝补偿6 | 0-200 | 165 | 起始回缝B（D）段针迹补偿，0～200动作逐步滞后；数值越大，B（D）段最后一针越长，C段第一针越短 |
| P34 | 定针缝运动模式选择 | A/M | A | A：轻触脚踏板，即自动执行定针缝动作 M：受脚踏板控制，可任意停止与启动 |
| P35 | 抬压脚时松线出力功能设定 | 0-1 | 1 | 0：抬压脚时松线出力功能关闭 1：抬压脚时松线出力功能开启 |
| P36 | 剪线时松线出力功能设定（松线器力道设置） | 0-11 | 5 | 0：无松线动作 1~11松线力度逐步变大 |
| P37 | 拨线/夹线出力功能设定 （夹线器力道设置） | 0-11 | 8 | 0：无动作； 1为拔线动作 2～11 夹线动作，动作力度逐步变大 |
| P38 | 切线出力功能设定 | ON/OFF | ON | ON：有切线动作 OFF：无切线动作 |
| P39 | 车缝途中停止时，压脚出力选择 | UP/DN | DN | UP：车缝停止时，自动抬起压脚 DN：车缝停止时，无自动抬压脚（由踏板后踏控制） |
| P40 | 切完线停止时，压脚出力选择 | UP/DN | DN | UP：切完线后，自动抬起压脚 DN：车切完线后，无自动抬压脚（由踏板后踏控制） |
| P41 | 车缝完成件数显示 |  | 0 | 车缝完成件数显示；长按减号键可计数清零； |
| P42 | 信息显示 |  |  | N01 电控版本号序列号 N02 选针盒版本号 N03 转速 N04 脚踏板AD值 N05 上定位机械角度 N06 下定位机械角度 N07 母线电压AD值 N12 膝靠位置感应器AD值 |
| P43 | 马达转动方向设定（正反转） | CCW/CW | CCW | CW：顺时针方向 CCW： 逆时针方向 |
| P44 | 停车力度 | 1-45 | 16 | 机器停车时的力度选择。 |
| P45 | 回缝出力的周期信号（%） | 1-50 | 25 | 回缝动作时，以周期性省电输出 |
| P46 | 切线后，反转提针角度的功能选择 | ON/OFF | OFF | ON：切完线后，自动作反转的功能。（角度由【P47.】调整决定）； OFF：无作用 |
| P47 | 切线后，反转提针角度的调整 | 50-200 | 160 | 切完线后，由针上算起以反向运转作提针的角度调整。 |
| P48 | 低速（定位速度）（rpm） | 100-500 | 210 | 定位速度设定 |
| P49 | 切线速度（rpm） | 100-500 | 300 | 调整切线周期时的电机速度 |
| P50 | 抬压脚全额出力时间（ms） | 10-990 | 250 | 压脚提升时序的动作时间 |
| P51 | 压脚出力的周期信号（%） | 1-50 | 25 | 压脚动作时，以周期性省电输出，避免压脚发烫 |
| P52 | 压脚下放时间（ms） | 10-990 | 120 | 延迟马达启动，确保压脚放下 |
| P53 | 半后踏取消抬压脚功能 | ON/OFF | OFF | ON：半后踏时，无抬压脚出力 OFF：半后踏时，有抬压脚出力 |
| P54 | 切线动作时间（ms） | 10-990 | 200 | 切线时序所需的动作时间 |
| P55 | 拨 / 扫线动作时间/ | 10-990 | 30 | 拨 / 扫时序的动作时间 |
| P56 | 开电后自动找上定位 | 0-2 | 1 | 0：始终不找上定位 1：始终找上定位 2：若电机已经处于上定位时不再找上定位（仅限于有磁钢电机） |
| P57 | 抬压脚保护时间（s） | 1-60 | 10 | 抬压脚保持时间后强制关闭 |
| P58 | 上定位调整 | 0-1439 | 1120 | 上定位调整，数值减少时会提前停针，数值增加时会延迟停针 |
| P59 | 下定位调整 | 0-1439 | 360 | 下定位调整，数值减少时会提前停针，数值增加时会延迟停针 |
| P60 | 测试速度（rpm） | 100-3700 | 2000 | 设置测试速度 |
| P61 | A项测试 | ON/OFF | OFF | A项测试选项，设定后将按【P60.】所设定之速度持续运行 |
| P62 | B项测试 | ON/OFF | OFF | B项测试选项，设定后将按【P60.】所设定之速度执行启动-车缝-停车-剪线的循环 |
| P63 | C项测试 | ON/OFF | OFF | C项测试选项，设定后将按【P60.】所设定之速度执行无定位动能的启动-车缝-停车的循环 |
| P64 | 测试B、C导通时间 | 1-250 | 20 | B、C项测试中，设置导通时间 |
| P65 | 测试B、C停车时间 | 1-250 | 20 | B、C项测试中，设置停车时间 |
| P66 | 机头保护开关检测 | 0-2 | 1 | 0：不检测 1：检测零信号 2：检测正信号 |
| P67 | 剪线保护开关检测 | ON/OFF | OFF | OFF：不检测 ON：检测 |
| P70 | 出厂机型选择 |  | 20 |  |
| P71 | 压脚释放缓冲占空比(%) | 0-50 | 2 | 压脚下放时的力度调整 |
| P72 | 上停针位校正 | 0-1439 | 0 | 调整上停针位，显示的数值会随手轮位置变化而变化，按“S”键可保存当前位置（数值）为上停针位 |
| P73 | 下停针位校正 | 0-1439 | 0 | 调整下停针位，显示的数值会随手轮位置变化而变化，按“S”键可保存当前位置（数值）为下停针位 |
| P74 | 机器编码1 |  |  |  |
| P75 | 机器编码2 |  |  |  |
| P76 | 倒缝全额出力时间(ms) | 10-990 | 250 | 倒缝开始动作时，全额出力的动作时间 |
| P77 | 自由缝连终止回缝停顿时间(ms) | 20-200 | 75 |  |
| P78 | 夹线器起夹角度 | 10-150 | 100 |  |
| P79 | 夹线器结束角度 | 160-359 | 270 |  |
| P80 | 剪线进刀角度 | 5-359 | 18 | 剪线进刀角度设置（下定位为0°计算） |
| P81 | 剪线开始加力角度 | 5-359 | 140 | 剪线加力角度设置（下定位为0°计算，需大于P80项参数值） |
| P82 | 剪线退刀角度 | 5-359 | 172 | 剪线退刀角度设置（下定位为0°计算，需大于P81项参数值） |
| P84 | 厚料开始加力角度 | 0-330 | 9 |  |
| P85 | 厚料结束加力角度 | 0-330 | 57 |  |
| P92 | 编码器绝对位置校正 |  | 160 | 读取编码器起始角度，出厂已设置，请勿随意更改（参数值不可手动更改，随意更改会导致控制箱、电机出现异常或损坏） |
| P99 | 终止回缝补偿C1 | 0-200 | 165 | 剪线后防脱线头模式下，终止回缝结束为C段时回缝一针的补偿 |
| P100 | 终止回缝补偿D1 | 0-200 | 185 | 剪线后防脱线头模式下，终止回缝结束为D段时回缝一针的补偿 |
| P101 | 松线开始角度 | 1-359 | 30 | 松线开始角度（下定位为0°计算） |
| P102 | 松线结束角度 | 1-359 | 180 | 松线结束角度（下定位为0°计算，需大于P101项参数值） |
| P117 | 压脚释放缓冲延迟时间（ms） | 0-990 | 12 |  |
| P120 | 油位报警开关检测 | 0-1 | 0 | 0：不检测 1：检测 |
| P121 | 剪线模式选针 | 0-3 | 2 | 0：普通模式 1：剪短线头模式 2：剪线后防脱线头模式 |
| P122 | 剪线后防脱线头模式，剪线前倒缝动作的时机 | 0-1439 | 1000 | 参数值越大剪线前一针的针距越大 |
| P123 | 剪短线头模式，剪线过程中倒缝动作的时机 | 0-100 | 0 |  |
| P125 | 膝靠感应器AD值1 | 0-1023 | 25 | 影响压脚抬升效果 |

3.错误代码表

| 错误码 | 内容 | 对策 |
| --- | --- | --- |
| E01 | 1）电源ON时，主电压检测过高 2）供应电源电压过高时 | 关闭系统电源，检测供应电源电压是否正确。（或是否超过使用规定的额定电压）。 若正确，请更换控制箱并通知厂方。 |
| E02 | 1）电源ON时，主电压检测过低 2）供应电源电压过低时 | 关闭系统电源，检测供应电源电压是否正确。（或是否低于使用规定的额定电压）。 若正确，请更换控制箱并通知厂方。 |
| E03 | 控制面板于CPU传输通信异常 | 关闭系统电源，检查控制面板接头是否松动或脱落，将其恢复正常后重启系统。若仍不能正常工作，请更换控制箱并通知厂方。 |
| E05 | 控速器接触异常 | 关闭系统电源，检查控速器接头是否松动或脱落，将其恢复正常后重启系统。若仍不能正常工作，请更换控速器并通知厂方。 |
| E07 | a)马达插头配线接触不良导致不转 b)车头机构死锁或马达皮带异物卷入卡死。 c)加工物过厚，马达扭力不足无法贯穿。 d模块驱动出力异常 | 转动机头电机手轮观察是否卡住。如卡住则先排除机头机械故障。 如转动正常，检查电机编码器接头和电机电源线接头是否松动。如有松动请修正。 如接触良好，检查供应电源电压是否异常或转速设置过高。如有请调整。 如正常，请更换控制箱并通知厂方。 |
| E08 | 连续手动倒缝超过15秒 | 倒缝电磁铁吸合时间过长，重启产品即可. 若重启产品后还是报E-08，请检查手动倒缝开关是否损坏。 |
| E10 | 电磁铁过流保护 | 关闭系统电源，检查电磁铁（电磁阀）连接线或电磁铁（电磁阀）是否损坏。 |
| E09 E11 | 定位信号异常 | 关闭系统电源，检查电机编码器接口是否松动或脱落，将其恢复正常后重启系统。若仍不能正常工作，请更换电机并通知厂方。 |
| E14 | 编码器信号异常 | 关闭系统电源，检查电机编码器接口是否松动或脱落，将其恢复正常后重启系统。若仍不能正常工作，请更换电机并通知厂方。 |
| E15 | 电力模块不正常过流保护 | 关闭系统电源，再重新开启。若仍不能正常工作，请更换控制箱并通知厂方。 |
| E17 | 机头保护开关没到正确位置 | 关闭系统电源，检查机头是否掀开，控制箱内滚珠开关是否移位或损坏。 |
| E20 | 开机电机启动失败 | 关闭系统电源，检查电机编码器接口和电机电源接口是否松动或脱落，将其恢复正常后重启系统。若仍不能正常工作，请更换控制箱并通知厂方。 |
| oil | 缝纫机油量过低 | 关闭电源，检查缝纫机油盘油量是否过低，将油量加满后重启系统。若仍不能正常工作，请更换油位感应器并通知厂方。 |

4.端口示意图

4.1：14P功能端口对应表

8P功能端口对应表

4.2端口名称

Safety Instruction

- Users are required to read the operation manual completely and carefully before installation or operation.

- All the instruction marked with sign   must be observed or executed; otherwise, bodily

injuries might occur.

- The product should be installed and pre-operated by well trained persons.

- For perfect operation and safety, it is prohibited that using extension cable with multi-outlet

for power connection.

- When connecting power supply cords to power sources, it is necessary to make sure that the  power voltage is lower than 250 VAC and matches the rated voltage indicated on the motor’s name plate.

※Attention: If the Control Box is AC 220V system, please don’t connect the Control Box to AC 380V power outlet. Otherwise, the error will occur and motor will not work. If that happens, please turn off the power immediately and check the power voltage.

- Don＇t operate in direct sun light，outdoors area and where the room temperature is over 45°C or below 5°C.

- Please avoid operating near the heater at dew area or at the humidity below 30% or above 95%.

- Don＇t operate in area with heavy dust, corrosive substance or volatile gas.

- Avoid power cord being applied by heavy objects or excessive force, or over bend.

- The earth wire of power cord must be connected to the system ground of the production plant by proper size of conductions and terminals. This connection should be fixed permanently.

- All the moving portions must be prevented to be exposed by the parts provided.

- Turing on the machine in the first time, operate the sewing machine at low speed and check the correct rotation direction.

- Turn off the power before the following operation：

a) Connecting or disconnecting any connectors on the control box or motor.

b) Threading needle.

c) Raising the machine head.

d) Repairing or doing any mechanical adjustment.

e) Machines idling.

14． Repairs and high level maintenance work should only be carried out by electronic technicians with appropriate training.

- All the spare parts for repair must be provided or approved by the manufacturer.

- Don’t use any objects or force to hit or ram the product.

Guarantee Time

Warranty period of this product is 1 year dated from purchasing, or within 2 years from ex-factory date.

Warranty Detail:

Any trouble found within warranty period under normal operation, it will be repaired free of charge. However, maintenance cost will be charged in the following cases even if within warranty period:

- Inappropriate use, including: wrong connecting high voltage, wrong application, disassemble, repair, modification by incompetent personnel, or operation without the precaution, or operation out of its specification range, or inserting other objects or liquids into the product.

- Damage by fire, Earth quake, lighting, wind, flood, salt corrosive, moisture, abnormal power

voltage and any other damage cause by the natural disaster or by the inappropriate environments.

- Dropping after purchasing or damage in transportation by customer himself or by customer’s shipping agency

Note:  We make our best effort to test and manufacture the product for assuring the quality. However, it is possible that this product can be damaged due to external magnetic interference and electronic static or noise or unstable power source more than expected; therefore the grounding system of operate area must guarantee the good earth and it’s also recommended to install a failsafe device.  ( Such as residual current breaker)

1.Button Displays and operating instructions

1.1.Key Description

| 名称 | 按键 | 注明 |
| --- | --- | --- |
| Function key enter parameter area |  | Under normal mode, press the [P] key to enter the user parameter mode |
| Enter and determine \ save button |  | Enter parameter values such items and their contents change after adjustment, need to press the [S] key to save the confirmation. |
| Set value increment / parameter increment key |  | 1．A、B、C、D、E、F、G、H section, increase the number of setting stitch . 2．Increase the parameter in Parameter selection. 3．Increase the setting value in Parameter value. |
| Set value decrement / decrement key parameters |  | 1．A、B、C、D、E、F、G、H decrease the number of setting stitch 2．Decrease the parameter in Parameter selection. 3．Decrease the setting value in Parameter value. |
| Start/End Back-Tacking Selection |  | Execution starting back seam B segment or execution starting back seam (A, B segment) 1Execution starting back seam (A, B segment) 2 times |
|  |  | Execution terminates back seam C segment or execution terminates back seam (C, D segment) 1 Execution terminates back seam (C, D segment) 2 times |
| Freedom sewing shortcuts |  | As the treadle is toed down, machine will start sewing. Once the treadle returns to neutral, machine will stop immediately. As the treadle is heeled back, machine will automatically start trimming cycle. |
| Some fixed stitch shortcuts |  | The implementation of paragraph E set needle function, when the display shows the icon, activate the E section of the needle function. |
| Continuous back seam shortcuts |  | Once the treadle is toed down, all the seams of Bar-Tacking will be completed with D times, and then the thread will automatically be trimmed. Note: When the Bar-Tacking Sewing starts, will not stop until the trimming cycle finished, except for the treadle heeled back to cancel the action. |
| Multi-section set needle shortcuts |  | Line multi-section stitching function, when the display shows the icon, the activation of multi-section needle stitch function. |
| Automatically trigger button |  | 1． In Free sewing: One touch of this key makes beep sound without any function also LED does not light up. 2．In Constant-Stitch Sewing: One shot to the pedal, stitches number of E, F, G or H will be automatically performed. Toe down the pedal again and again to finish the rest sections until it finish pattern. |
| Press the lift foot shortcuts |  | 1、When the icon is on, the presser foot is automatically lifted after cutting. 2、When the icon is on, the presser foot automatically lifts when the motor stops in the sewing. 3、When both icons are on, the presser foot is automatically lifted when the motor is stopped and the thread is cut. 4、When the 2 icon is off, there is no automatic presser foot function. |
| Thread clamping function / lifting the foot when the loose line function shortcut keys |  | 1, the corresponding icon is on, the thread clamp function is turned on. 2, the corresponding icon does not shine, no clamp function. |
| Shortcut function |  | 1. Set the use or cancel tangent function. 2. When the corresponding icon is off, it means that the corresponding function is disabled. |
| Slow play seam shortcuts |  | 1．The corresponding icon lights, slow starting sewing open. 2．The corresponding icon is not lit, no slow-starting sewing function. |
| Stop the needle position switch key |  | 1：The icon lights up to indicate the stop position at stop 2：The icon indicates that the needle stops at the next stop |
| Fill the needle button |  | If you click, you can make a needle |

2     User Parameter &Technician Parameter

| Parameter | Parameter Function | Range | Default | Description |
| --- | --- | --- | --- | --- |
| P01 | Maximum Sewing Speed（rpm） | 100-3700 | 3700 | Maximum speed of machine sewing |
| P02 | Speed Curve Adjustment（%） | 10-100 | 80 | The Lager the value, the faster to increase speed |
| P03 | Needle UP/ DOWN | UP/DN | DN | UP: Needle Stops at Up Position DN: Needle Stops at Down Position |
| P04 | Start Back-Tacking Speed（rpm） | 200-3200 | 1800 | Start Back-Tacking Speed Adjustment |
| P05 | End Back-Tacking Speed（rpm ） | 200-3200 | 1800 | End Back-Tacking Speed Adjustment |
| P06 | Bar-Tacking Speed（rpm） | 200-3200 | 1800 | Repeat Bar-Tacking Speed Adjustment |
| P07 | Soft Start Speed（rpm ） | 200-1500 | 400 | Soft Start Speed Adjustment |
| P08 | Stitch Numbers for Soft Start | 0-99 | 2 | Soft Start Stitches Setting ( one unit = half stitch) |
| P09 | Automatic Constant-Stitch Sewing Speed（rpm） | 200-4000 | 3700 | Constant-Stitch sewing speed【034.SMP】 is set at A(or when one shot signal is active) |
| P10 | Automatic End Back-Tacking Sewing(Can invalidate the stitch correction function) | ON/OFF | ON | The Stitch-Correction is valid in sewing stop. Note: Valid only when the【0.11.RVM】must set on B ON: Invalid (Constant-Stitch sewing, it can automatic continue action as CD function) OFF: Valid (Can’t continue execute CD function) |
| P11 | Back-Tacking Mode Selection | J/B | J | J：JUKI Mode (In the middle of the car to stop the middle of the time to stop when the inverted seam）B：BROTHER Mode (That is, in the vehicle to perform the reverse operation of the seam, in the end of the time to stop the needle |
| P12 | Start Back-Tacking Mode Selection | 0-1 | 1 | A：One shot to pedal, it will automatic execute Start Back-Tacking. M：Pedal-controlled and motor can stop arbitrarily |
| P13 | Mode Selection at the end of Start Back-Tacking | CON/STP | CON | CON：At the end of Start Back-Tacking, machine continues sewing if pedal pressed or START signal on ( standing operation) STP：At the end of Start Back-Tacking, machine stops |
| P14 | Soft Start | ON/OFF | ON | ON: Slow start feature is turned on. OFF: Slow start function off. |
| P15 | Make up pin mode | 0-4 | 2 | 0: Semi-pin；1: a pin 2：Continuous filling half needle 3：Continuous injection |
| P18 | Stitch Balance for Start Back-Tacking 1 | 0-200 | 131 | A starting back seam segment stitches compensation 0-200 movement gradually lag; the larger the value, A short last longer needle, B section of the first needle is shorter |
| P19 | Stitch Balance for Start Back-Tacking 2 | 0-200 | 165 | Starting back seam B segment stitches compensation 0-200 movement gradually lag; the larger the value, paragraph B last longer needle |
| P20 | Mode Selection for End Back-Tacking | 0-2 | 1 | A：Pedal full heeling ,it will automatic execute end Back-Tacking |
| P24 | Foot pedal reverse voltage | 30-500 | 110 |  |
| P25 | Stitch Balance for End Back-Tacking 3 | 0-200 | 131 | Starting back seam segment stitches compensation C, 0-200 movement gradually lag; the larger the value, the shorter the C section of the first pin |
| P26 | Stitch Balance for End Back-Tacking 4 | 0-200 | 165 | D starting back seam segment stitches compensation 0-200 movement gradually lag; the larger the value, C section last a longer needle, the first needle is shorter segment D |
| P28 | Mode Selection for Bar-Tacking | 0-2 | 1 | Continuous back seam segment, rewind solenoid operation timing: 0: controlled by the pedal can be arbitrarily stopping and starting; 1: Touch the pedal, automatically performs back-tacking action; 2: pause mode |
| P29 | Tangent after braking force | 1-45 | 20 |  |
| P30 | Thick material angle | 0-100 | 0 | The larger the value the greater the intensity, the adjustment is too large may cause the motor abnormalities. |
| P31 | Cutting angle | 0-100 | 30 | The larger the value the greater the intensity, the adjustment is too large may cause the motor abnormalities. |
| P32 | Stitch Balance for Bar-Tacking 5 | 0-200 | 121 | Start back-tacking A (C) paragraph stitch compensation, 0-200 movement gradually lag; the larger the value, A (C) the last paragraph of a needle longer; B (D) of the first paragraph, the shorter pin |
| P33 | Stitch Balance for Bar-Tacking 6 | 0-200 | 165 | Starting back seam B (D) segment stitch compensation, 0-200 movement gradually lag; the larger the value, B (D) last paragraph a longer needle, C section of the first needle is shorter |
| P34 | Mode Selection for Constant-Stitch Sewing | A/M | A | A：One shot to pedal, it will automatic execute Constant-Stitch M：Pedal-controlled and motor can stop arbitrarily |
| P36 | Slack line output function setting(loose line power set) | 0-11 | 5 | 0: no loose wire operation 1 to 11 and gradually increases the intensity of loose wire |
| P37 | Wiper Function Selection or Thread Clamp Pressure Setting | 0-11 | 8 | 0 : No Action 1: Wiper Action 2-11: Thread Clamp action and the pressure gradually increased） |
| P38 | Trimmer Function Selection | ON/OFF | ON | ON：Trimmer Valid OFF: Trimmer Invalid |
| P39 | Presser Foot UP / Down at intermediate stop | UP/DN | DN | UP：Presser foot goes up automatically DN：Presser foot keeps down （Controlled by heeling pedal） |
| P40 | Presser Foot UP / Down after Trimming | UP/DN | DN | UP：Presser foot goes up automatically DN：Presser foot keeps down（Controlled by heeling pedal） |
| P41 | Display the sewing finished quantity |  | 0 | Counting the finished-sewing quantity |
| P42 | Information Display |  |  | NO1 Electrically controlled version serial numbers NO2 Selected needle cassette version NO3 Speed NO4 Pedals AD, NO5 Positioning angle NO6 Under the positioning angle NO7 Bus voltage AD N12 Knee position sensor AD |
| P43 | Setting Direction of Motor Rotation | CCW/CW | CCW | CW：Clockwise CCW： Counter Clockwise |
| P44 | Parking efforts | 1-45 | 16 | Efforts to stop the machine when selecting |
| P45 | Back-seam operation duty cycle (%) | 1-50 | 25 | Back-seam action to periodic power output |
| P46 | Motor stops with a reverse angle after trimming | ON/OFF | OFF | ON：It will automatic as reverse function after trimming (angle adjustment according to the parameter【047.TR8】 OFF：No Function |
| P47 | Adjustment of reverse angles after trimming | 50-200 | 160 | Adjusting at reverse direction after trimming |
| P48 | Low (Positioning) Speed（rpm ） | 100-500 | 210 | Setting Positioning Speed |
| P49 | Trimming Speed（rpm） | 100-500 | 300 | Adjusting trimming speed |
| P50 | The time of Foot lifting | 10-990 | 250 | Adjustment of foot lifting action |
| P51 | Lift foot full force time（%） | 1-50 | 25 | Adjustment for Duty-Cycle of Foot Lifter / Back-Tacking (Fine tuning can reduce the over-heating) |
| P52 | The time of Foot down | 10-990 | 120 | Delay starting motor, ensure that the foot is put down. |
| P53 | Cancel Foot Lifting when Half-Heeling the Pedal | ON/OFF | OFF | ON：Pedal half heeling without foot lifting function. OFF：Pedal half heeling with foot lifting function |
| P54 | Trimming Time（ms） | 10-990 | 200 | Trimming sequence time setting |
| P55 | Setting Wiper Timing | 10-990 | 30 | Wiper sequence setting |
| P56 | Needles Goes Up Automatically as Power turned on | 0-2 | 1 | 0: always not to find a position 1：: always looking for positioning 2：If the motor is positioned on the no longer find location (only with magnet motor) |
| P57 | Protection time for foot lifter（S） | 1-60 | 10 | It will automatic come down when foot lifter keep lift over the setting time. |
| P58 | Up Position Adjustment | 0-1439 | 1120 | Up Position Adjustment The needle will advance stop when the value decreased. The needle will delay stop when the value increased. |
| P59 | Down Position Adjustment | 0-1439 | 360 | Down Position Adjustment The needle will advance stop when the value decreased. The needle will delay stop when the value increased. |
| P60 | Testing Speed（rpm ） | 100-3700 | 2000 | Setting testing speed. |
| P61 | Testing A | ON/OFF | OFF | Option of Testing A, after setting press 【060. TV】to set the speed keep running. |
| P62 | Testing B | ON/OFF | OFF | Option of Testing B, after setting press 【060. TV】to set the speed execute the cycle of Start – Sewing –Stop - Trimming |
| P63 | Testing C | ON/OFF | OFF | Option of Testing C, after setting press【060. TV】to set the speed execute the cycle of Start – Sewing –Stop without positioning function |
| P64 | Running Time of Testing B and C | 1-250 | 20 | Setting running time of testing B and C |
| P65 | Stop Time of Testing B and C | 1-250 | 20 | Setting stop time of testing B and C |
| P66 | Machine Protection Switch Testing | 0-2 | 1 | 0：Disable， 1：Testing zero signal， 2：Testing positive signal |
| P67 | Trimming Protection Switch Testing | ON/OFF | OFF | OFF：Disable ON：Enable |
| P70 | The factory Type Selection |  | 20 |  |
| P71 | Presser foot release buffer duty cycle (%) | 0-50 | 2 | Efforts to ease foot pressure release time |
| P72 | The needle position correction | 0-1439 | 0 | Hand rotation manual to the appropriate position, press S key to save |
| P73 | Under needle position correction | 0-1439 | 0 | Hand rotation manual to the appropriate position, press S key to save |
| P76 | Backstitch output of full time (ms) | 10-990 | 250 |  |
| P77 | Freedom sew back seam even terminate pause time (ms) | 20-200 | 75 |  |
| P78 | The Thread Clamp release angle | 10-150 | 100 | The positioning angle of starting clamp |
| P79 | Clamp start action angle | 160-359 | 270 | The positioning angle of release |
| P80 | Shear line infeed is angle | 5-359 | 18 | Shear line infeed is angle setting (under defined as 0 °) |
| P81 | Cut the line start angle | 5-359 | 140 | Afterburner trimming angle setting |
| P82 | Retract angle cut line | 5-359 | 172 | Afterburner trimming angle setting |
| P84 | Thick start angle | 0-330 | 9 |  |
| P85 | The thick end angle | 0-330 | 57 |  |
| P92 | Encoder start angle |  | 160 |  |
| P101 | Loose line starting angle | 1-359 | 30 | Song line start angle (defined as 0 ° under calculation) |
| P102 | Loose end angle | 1-359 | 180 | Loose wire end angle (defined as 0 ° under calculation) |
| P117 | Release the presser foot buffer delay time (ms) | 0-990 | 12 |  |
| P120 | Oil alarm switch detects | 0-1 | 0 | 0: Not detected 1: detected |
| P121 | Trimming needle selection mode | 0-3 | 2 | 0: Normal mode 1: cut thread mode 2: off thread trimming defense mode 3: Reserved |
| P122 | Timing off thread trimming defense mode, before trimming back tack action | 0-1439 | 1000 | A needle before the needle parameter values greater the distance the greater the cut line |
| P123 | Cut the thread mode, trimming back tack during operation timing | 0-100 | 0 |  |
| P125 | Knee by inductor value AD 1 | 0-1023 | 25 | Effect lifter effect |

3    Error Code List

| Error Code | Problem | Strategies |
| --- | --- | --- |
| E1 | Power Module is faulty. Abnormal over current or voltage. Resistor is damaged or F1 fuse is blown. | System will be shut down until the power resets on. Please check the power board in detail. |
| E2 | 1）When power on, detected main voltage too low 2）Connect the wrong voltage, too low. | Moto and machine will be shutting down. Please check the AC power. (Too low) Please check the main pc board. |
| E3 | Operation Box linked to CPU interface had communication error. | Motor and machine will be shutting down. Please check the operation box. |
| E5 | The connection of the Foot Pedal error | Motor and machine will be shutting down. Please check the connection of the Foot Pedal or the problem of it |
| E7 | a) Bad connection at the motor connector. b) Machine locked or object stuck in the motor pulley. c) Sewing material is too thick. d Module output is abnormal. | Head rotation motor handwheel see if stuck. As the first rule nose stuck mechanical failure. As normal rotation, check the motor and motor encoder connector power cord connector is loose. Please correct if loose. As good contact, check the power supply voltage is abnormal or speed is set too high. If yes, please adjust. As normal, replace the control box and inform the manufacturer. |
| E8 | Manual Back-Tacking lasts for 15 sec. | Reverse stitching solenoid pull too long, you can restart the product. If the product or reported after the restart E-08, check the manual back tack switch is damaged. |
| E09 E11 | Positioning signal error | Power off the system, check the motor encoder interface is loose or fall off, it was back to normal after restarting the system. If it still does not work, replace the motor and inform the manufacturer |
| E14 | Encoder signal error | Power off the system, check the motor encoder interface is loose or fall off, it was back to normal after restarting the system. If it still does not work, replace the motor and inform the manufacturer. |
| E15 | Power module abnormal over-current protection | Power off the system, then on again. If it still does not work, replace the control box and inform the manufacturer. |
| E17 | Head protection switch is not in the correct position | Power off the system and check whether the nose open, ball switch control box whether displaced or damaged. |
| E20 | Power motor failed to start | Power off the system, check the motor encoder interface and motor power connector is loose or fall off, it was back to normal after restarting the system. If it still does not work, replace the control box and inform the manufacturer. |
| oil | Sewing machine oil is too low | Turn off the power and check the oil pan sewing machine oil is too low, after the oil fill reboot the system. If it still does not work, replace the oil level sensor and inform the manufacturer. |

4. Port Outline Diagram

4. 1  14P function port table illustration

8P function port table illustration

4.2  Port Name